## Slide 1
Here is where your presentation begins
GRADUATION PROJECT
Topic: DESIGN AND MANUFACTURE PICKLEBALL MACHINE
UNIVERSITY OF TECHNOLOGY AND EDUCATION
FACULTY OF MECHANICAL ENGINEERING
Instructor: TS. ĐỖ VĂN HIẾN
Performer: NGUYỄN QUANG GIAO MSSV: 19146121
BÙI TRƯƠNG VĨNH PHÚC MSSV: 20146518
Ho Chi Minh, January 18, 2025

## Slide 2
Business Report of Company Department Report of Company Department
Project Presentation Content
I: Reasons for choosing the topic, purpose and requirements of the project
II: Design and manufacture hardware structures
III: Algorithm and Control
IV: Experiment
V: Conclusion

## Slide 3
CONTENTS
I: Reasons for choosing the topic, purpose and requirements of the project
In Vietnam, Pickleball began to appear in 2018 and has quickly become popular. Many playgrounds and Pickleball clubs have been established in Hanoi, Ho Chi Minh City and other provinces.
With the continuous increase in players, the supporting equipment is still limited, including ball pickers.
With the desire to create a ball picker for players, we decided to design and manufacture a Pickleball picker machine.
Reasons for choosing the topic
a. Practical needs from pickleball players
b. The Urgency of Improving Training Efficiency
c. Applicability and commercial potential
d. Exploiting technology and technical innovation
e. Contribute to promoting community sports movement
f. Academic significance and personal skill development

## Slide 4
I: Reasons for choosing the topic, purpose and requirements of the project
Requirements of the project
˗Limited working area: 40m2.
˗Operating conditions: Outdoors, no rain.
˗Operates on flat terrain.
˗Maximum robot operating time: 45 minutes.
Purpose of project

## Slide 5
CONTENTS
II: Design and manufacture hardware structures
After considering the methods,
we decided to choose “Paddle Methods” to collect the ball.
-With strong rotation force, when the pickleball to
touch the fan blade to easily collect the pickleball inside.
-The structure of the paddle wheel is
relatively simple, easy to manufacture,
maintain and can change the size of the
fan blade depending on the size of the ball easily.
Paddle wheel

## Slide 6
CONTENTS
II: Design and manufacture hardware structures
Design and manufacture Ball collection mechanism
Design in software
Actual construction

## Slide 7
CONTENTS
II: Design and manufacture hardware structures
Image processing
Image processing is the process of converting images into digital form and performing operations to extract useful information from that image.

## Slide 8
CONTENTS
II: Design and manufacture hardware structures
Image processing
Step 1: Image acquisition
Dimensions: 79mm x 31mm x 38.5mm.
Video resolution: 1080p.
Photo resolution: 10MP.
Frame rate: 60FPS.
Color: Black - Resolution: HD 1080
Connection: USB 2.0
Cable length: 1.5m
Webcam HD 1080p
Webcam HD 1080p

## Slide 9
CONTENTS
II: Design and manufacture hardware structures
Image processing
Step 2: Image processing
Before and after using Gaussian filter
Result with pickleball

## Slide 10
CONTENTS
II: Design and manufacture hardware structures
Image processing
Step 3: Image converter
Convert the RGB color space to HSV color space

## Slide 11
II: Design and manufacture hardware structures
Image processing
Step 4: Identification and classification
Output Results
Canny edge detection
Good noise immunity
Minimal error
-Use Hough Transform and
Color Segmentation
- Determine the position of the ball

## Slide 12
CONTENTS
II: Design and manufacture hardware structures
Raspberry Pi is a small-sized computer (SBC - Single Board Computer)
Raspberry Pi 4 Model B 8gb
Easy Access: With its affordable price, Raspberry Pi allows
everyone, especially students and beginners, to have access
to microcontroller technology and embedded computers.
Convenience: Raspberry Pi is compact in size, easy to
carry and use anywhere.
Many applications such as:
-Build Projects IoT (Internet of Things)
-Control Small Robots
-Home Automation
-Web Servers

## Slide 13
CONTENTS
II: Design and manufacture hardware structures
Waveshare 7inch LCD
120W Power Bank
Similar to previous products, 120W 20000mAh power bank is equipped with Li-Po (Lithium Polymer) battery core from leading manufacturers such as LG/Panasonic.
Datasheet:
- Slim and lightweight design
- Battery capacity: 20.000 mAh
- Fast charging speed with a capacity of 18 W
- Includes 2 Micro USB and Type C input ports
- Equipped with 2 convenient USB output ports that can charge 2 devices at the same time.
7inch HDMI LCD touch screen allows Raspberry Pi to be connected via HDMI port, 800×480 resolution capacitive touch, supports Raspberry Pi and can also be used as a computer monitor. In this project, Waveshare screen will be connected to Raspberry Pi to display the image of the environment in front of the camera when detecting for the purpose of processing Pickleball image.

## Slide 14
CONTENTS
II: Design and manufacture hardware structures
Choose MCU
Arduino Uno R3
Arduino Uno R3 is one of the most popular boards in the Arduino product line, widely used in electronics projects and embedded programming
Datasheet of Arduino Uno R3

## Slide 15
CONTENTS
II: Design and manufacture hardware structures
Motor control
L298N
Datasheet
-Main IC is L298 – Dual Full Bridge Driver.
-Input voltage from 5 to 30VDC.
-Maximum power is 25W for each bridge (note that power is calculated by current multiplied by voltage, so when the input voltage is higher, the current is smaller, the power remains the same at 25W).
-Maximum current for each H-bridge is 2A.
-Logic voltage levels: Low from -0.3V to 1.5V, High from 2.3V to Vss (ground).
-The size of the circuit is 43x43x27mm.
The L298N DC motor control module can control two DC motors, the maximum current is 2A per motor, this module includes a protection diode and a 7805 power IC to supply 5VDC to other modules (use this 5V only if the power supply is <12VDC). This circuit is simple and easy to use, has a low price and is the best choice in the price range.

## Slide 16
CONTENTS
II: Design and manufacture hardware structures
Select motor
We chose motor JGA25 130RPM for the ball picker project.
Datasheet:
-Supply voltage: 6-18VDC
-Speed after gearbox: 130rpm
-Torque: 5 kg.cm = 0.49 N.m
-No-load current: 50mA
The JGA25-370 motor is a popular choice for applications requiring high torque at low speeds. Great for robot car model projects
Motor JGA25 130RPM
Wheel Hex Joint 68mm– Type 3
Choose Wheel Hex Joint 68mm– Type 3 for this project.
The wheel uses a common hexagon joint (12mm) which is easy to assemble and apply to the design.
Datasheet:
-Material: Hard plastic, foam padding, good rubber.
-Diameter: 68mm.
-Wheel width: 27mm
Select wheel

## Slide 17
CONTENTS
III: Design and Construction
Block diagram of the system

## Slide 18
CONTENTS
III: Design and Construction
System wiring diagram

## Slide 19
CONTENTS
III: Design and Construction
Robot design on software
Overall Robot Drawing
Robot drawing top view

## Slide 20
CONTENTS
III: Design and Construction
Robot design on software
Ball collection mechanism
Ball and accessory storage bin

## Slide 21
CONTENTS
III: Design and Construction
  Construction
Step 1: Choose materials for the robot in the topic we will use mica because it is easy to buy, not too heavy.
Step 2: Choose the size of the robot to proceed to cut mica and assemble according to the desired size: Robot frame has a size of 30x45cm.
Robot frame
Robot wheel
Step 3: Install the wheels, mount the motor to the
4 motors to make 4 wheels for the robot to move.

## Slide 22
CONTENTS
III: Design and Construction
  Construction
Component compartment
Ramp
Step 4: Install the component compartment for the robot, this will hold all the components of the system
Step 5: Install a ramp to help roll the ball in for retrieval.

## Slide 23
CONTENTS
III: Design and Construction
  Construction
Step 6: Install the camera mount for the robot
The camera will be installed at the highest part
of the robot to have the widest viewing angle,
easily finding and identifying the pickleball.

## Slide 24
CONTENTS
III: Design and Construction
  Construction
Step 7: Cut and paste the pickleball collecting mechanism for the robot
Pickleball chute
Horizontal shaft mounting of ball collecting motor
Step 8: Attach the horizontal shaft to the ball
collecting motor

## Slide 25
CONTENTS
III: Design and Construction
  Construction
Connect the wires according to the diagram
Step 9: Connect the wires as designed

## Slide 26
CONTENTS
III: Design and Construction
  Construction
Robot complete
Step 10: Complete the overall robot

## Slide 27
CONTENTS
III: Design and Construction
Algorithm flowchart

## Slide 28
CONTENTS
III: Design and Construction
Connect Raspberry Pi and Arduino Uno via USB port
Passing data from Python to Arduino
- serial.Serial(): initialize the function of the Serial class
in the pyserial library
- '/dev/ttyACM0': connect the device's serial port
- 9600: This is the baud rate

## Slide 29
CONTENTS
III: Design and Construction
  Communicating L298N DC Motor Control Module with Arduino
Motor control logic board
Pinout of L298N DC Motor Control Module
From here, the Arduino will control the motor module to control the motor as we have programmed.
-Signal 1,2, the Robot will turn left
-Signal 3,4,5 the Robot will go straight
-Signal 6,7 the Robot will turn right.

## Slide 30
CONTENTS
III: Design and Construction
  Control robot via app
Create Web Dashboard
Create a Blynk account

## Slide 31
CONTENTS
IV: Experiment
Detect ball position

## Slide 32
CONTENTS
IV: Experiment
Detect ball position

## Slide 33
CONTENTS
IV: Experiment
Detect ball position

## Slide 34
CONTENTS
IV: Experiment
Auto mode

## Slide 35
CONTENTS
IV: Experiment
Manual mode

## Slide 36
CONTENTS
IV: Experiment
After testing in left, straight, and right positions, the robot can work quite well.
With 10 tests, the robot has the following results:
Conclusion: Testing with the pickleball in all 3 directions,
the robot recovered the ball with a fairly high rate of 87%.

## Slide 37
CONTENTS
V: Conclusion
-The model runs exactly as the topic requires
-Image processing correctly identifies the pickleball according to the problem requirements
-Pickleball retrieval is quite accurate with relative speed
-Precise manual mode control
Conclusion
Advantages
-The robot has a relatively moderate size to be able to hold many balls.
-The hardware is made of mica, lightweight cardboard and is cheap
-The processing speed is quite fast and relatively accurate
-Can be controlled via app from phone
-Lack of calculation experience makes the robot unstable
-Operating time is not long-lasting
-There are also limitations in the camera's vision so sometimes the ball can be next to the side of the car without the car detecting it.
-The robot can collect balls in areas close to the wall, but it still cannot reach the corner areas to collect balls.
Disadvantages

## Slide 38
CONTENTS
V: Conclusion
Difficulties in implementing the project
-Difficulty in choosing suitable materials and testing the ball collecting mechanism, when assembling the paddle wheel is not firm, leading to deformation or popping out of the paddle wheel while collecting the ball. The paddle wheel speed must be reasonable, if the speed is too high, the ball will not have time to go inside but will be continuously pushed out by the paddle wheel, if the speed is too low, there will not be enough force to push the ball in.
- The ball guide mechanism has problems that can cause the ball to get stuck when the paddle wheel is rotating.
- Some devices are purchased old, so they cannot be used well and it takes time to buy new devices.
- Difficulty in finding reference documents and available project information sources.
When experimenting with moving, there are problems such as not being able to locate the ball position, the vehicle does not move in the desired direction in the code, there are many errors in programming and battery capacity problems, so the engine cannot operate strongly enough and long enough.

## Slide 39
CONTENTS
V: Conclusion
Development direction
-Find ways to optimize accuracy, ball detection and ball picking speed.
-Create a new ball collecting mechanism that can collect balls lying in the corner of walls or corners of strange objects.
-Can withstand impact when hit by a ball.
-Make a phone application that connects to the robot to monitor parameters such as battery, number of balls in the basket, and alert when there is a problem.
-Design to increase the size of the basket to hold more balls.
-Add ambient sensors to continuously avoid obstacles or when approaching walls.

## Slide 40
Thank you